## Slide 1: 2d-1r-isotropic-constant-star

## Slide 2: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 441x441
ECM = 18 cy => 6*8/18*2.59 = 6.91 GFLOP/s (1151 MLUP/s)
  based on load kernel with 57.39 GB/s
Roofline = 7.54 GFLOP/s (1256 MLUP/s)
  Due to L1 transfer bottleneck
  AI=0.18
  Saturation = 1 core
Execution = 6.95 GFLOP/s (1158 MLUP/s)

## Slide 3: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 883x883
ECM = 18 cy => 6*8/18*2.59 = = 6.91 GFLOP/s (1151 MLUP/s)
  based on load kernel with 57.39 GB/s
Roofline = 7.54 GFLOP/s (1256 MLUP/s)
  Due to L1 transfer bottleneck
  AI=0.18
  Saturation = 1 core
Execution = 7.57 GFLOP/s (1262 MLUP/s)

## Slide 4: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 1767x1767
ECM = 29.8 cy => 6*8/ 29.8 *2.59 = 4.17 GFLOP/s (695 MLUP/s)
  based on load kernel with 63.90 GB/s
  Saturation = 3.8 cores
Roofline = 3.91 GFLOP/s (652 MLUP/s)
  Due to MEM transfer bottleneck
  AI=0.25
  Saturation = 1 core
Execution = 3.65 GFLOP/s (609 MLUP/s)

## Slide 5: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 3000x3000
ECM = 29.8 cy => 6*8/ 29.8 *2.59 = 4.17 GFLOP/s (695 MLUP/s)
  based on load kernel with 63.90 GB/s
  Saturation = 3.8 cores
Roofline = 3.91 GFLOP/s (598 MLUP/s)
  Due to MEM transfer bottleneck
  AI=0.25
  Saturation = 1 core
Execution = 3.48 GFLOP/s (580 MLUP/s)

## Slide 6: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 3534x3534
ECM = 29.8 cy => 6*8/ 29.8 *2.59 = 4.17 GFLOP/s (695 MLUP/s)
  based on load kernel with 63.90 GB/s
  Saturation = 3.8 core
Roofline = 3.91 GFLOP/s (598 MLUP/s)
  Due to MEM transfer bottleneck
  AI=0.25
  Saturation = 1 core
Execution = 3.37 GFLOP/s (562 MLUP/s)

## Slide 7: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 12000x12000
ECM = 33.8 cy => 6*8/ 33.8 *2.59 = 3.68 GFLOP/s (613 MLUP/s)
  based on load kernel with 63.90 GB/s
  Saturation = 4.3 cores
Roofline = 3.91 GFLOP/s (598 MLUP/s)
  Due to MEM transfer bottleneck
  AI=0.25
  Saturation = 1 core
Execution = 3.11 GFLOP/s (519 MLUP/s)

## Slide 8: Analysis on Mini-HPC (@2.59 GHz)
FLOP = 6
Dimension = 40000x500
ECM = 25.8 cy => 6*8/ 25.8 *2.59 = 4.09 GFLOP/s (682 MLUP/s)
  based on load kernel with 63.90 GB/s
  Saturation = 3.3 cores
Roofline = 3.91 GFLOP/s (598 MLUP/s)
  Due to MEM transfer bottleneck
  AI=0.25
  Saturation = 1 core
Execution = 3.88 GFLOP/s (646 MLUP/s)